## Slide 1: The HADES P beam line: an update
T. Hennino (IPN Orsay)
XXVII HADES Collaboration Meeting
München, 5-7/2/2014
With E. Atomssa, W. König, B. Ramstein, P. Salabura, J. Biernat

## Slide 2: Brief reminder of the problem
Find the ‘best’ tuning of the ‘beam line’ that fulfills
  Highest flux at the HADES target (33.465 m away from the production target)
  Best possible focus and achromaticity at the HADES target point
  Compact geometry to keep within detector and LH2 geometrical sizes
  Resolution on the individual pion momentum
    Identification of reaction through MM or IM cuts
    Energy scan
  Impact point resolution to eliminate background reactions induced in LH2 solid parts

## Slide 3
The HADES beam line: horizontal view
Q1
Q2
FOPI
D1
Q3
Q4
Det 1
Q5
Q6
HADES cave
In the old configuration
Production target
D2

## Slide 4
The HADES beam line: standard setting SET 6
Detector 2
Q8
H Foc
Q9
V Foc
Q7

## Slide 5: Transmission versus step number
Qua 2
Dip 1
Det 1
HADES
Qua 7
Dip 2
Acceptance normalised to the input conditions:
- 6 % < d < + 6 %
- 10 mrad < q < + 10 mrad
- 50 mrad < j < + 50 mrad
Average transmission
18.5 %
SET 6: FDF

## Slide 6: x-y (in mm) at HADES_LH2 with |x|,|y|< 6 mm
Fraction left (in %)
1%
7%
14%
73%
31%
56%
95%
100%
100%
42%
22%
13%
10%
-6%
-4%
-2%
0%
2%
4%
6%
(# of pions at HADES with |x|,|y| < 6 mm) / (# of pions after the last quadrupole) = 66 %
 34 % of the pions will interact with the non-LH2 target material
Overall pion transmission = (# of pions at HADES with |x|,|y| < 6 mm) / (# of pions emitted at the production target) = 18.6 %
z: log scale
m = 0.46 %
s = 1.52 %
d (%)
Global transmission
Losses between Q9 and HADES target

## Slide 7: How to extract d (and qi, ji and yi )
Coupling to j
Coupling to q
1st order + 2nd order terms × 10
System of 4 non-linear equations with
4 unknown qi , yi , ji and d ( xi term ‘neglected’)
 solved iteratively
H and V are strongly coupled + chromatic terms in vertical
Chromatic 1st order
HV coupling
Chromatic 2nd order
Chromatic 2nd order V coupling
HV coupling
2 equations ( one measured X position at detector 1, another one at detector 2) with 8 terms
2 equations (one measured Y position at detector 1, another one at detector 2) with 7 terms

## Slide 8: p momentum resolution
pp=0.65 GeV/c
sx=0.5 mm
pp=1.3 GeV/c
sx=1.0 mm
pp=1.3 GeV/c
sx=0.5 mm
At d ≈ 1.5% (shift due to off focus detector1)
  sp scales with sx
  sp = 0.11%
  multiple scattering negligible
At large |d|
  sp dominated by multiple scattering effects
  sp weakly sensitive to sx
  sp scales with 1/p
  Within ± 2strans :
    sp < 0.2 %
± 2 s transmissionband
Contributes weakly (1/3) to the
MM resolution in the reaction
p- p  e+ e- n
(HADES resolution dominated)
- - - no ms

## Slide 9: X-vertex resolution at HADES target point
pp=0.65 GeV/c
sx=0.5 mm
pp=1.3 GeV/c
sx=1.0 mm
pp=1.3 GeV/c
sx=0.5 mm
At d ≈ 0%
no 2nd order chromatic terms
Effect of Coulomb scattering = 0.
 resolution is ~ proportional to horizontal primary beam size sx
At large |d|
Coulomb scattering dominant
resolution is almost independant on the horizontal primary beam size sx
Scales linearly with 1/p
Good selection of LH2 events
  Within ± 2strans : sx < 2 mm
± 2 s transmissionband

## Slide 10: ‘Measuring’ the 15 coefficients
Incident proton beam 4.3 GeV/c, pion production target off
Measuring the dispersive terms: T16, T36, T166, T366
  tune second part at d = -4%, -2%, 0%, 2% and +4%
Measuring the <x/y|x/q..> terms: T11, T12, T32, T116, T126
  qi = [-8, 0, 8] mrad , xi = [-2, 0, 2] mm
  d = 0 and 2%
Measuring the <x/y|y/j..> terms: T14, T33, T34, T146, T336, T346
  ji = [-7, 0, 7] mrad , yi = [-1, 0, 1] mm
  d = 0 and 2%
Index
numbering scheme
X
q
Y
j
-
d
A few shifts (during daytime) with beam experts and pion tracker (HADES detectors turned off)

## Slide 11: Measuring the dispersive terms
Minimize:
And extract horizontal and vertical dispersive coefficients T16, T166, T36, T366 and a possible offset X0 (misalignment of magnet and/or detectors)
In total 12 parameters = 3(XO, T16, T166) × 2(X and Y) × 2 (det1 and det2)
with 5 different settings of the HADES beam line
H plane
V plane

## Slide 12: How to extract the term involving q and j
Use the same 4.3 GeV/c proton beam on the pion production target
Can we focus the beam at the production target with different x and q for T1j coefficients, resp. y and j for T3j coefficients
  Use the kickers (4 available) along the beam line
  Use position sensitive device
    Grid in X and Y (good position resolution ~0.2 mm)
    Scintillating detector at the p production target
      No calibration on x impact possible
      Calibration on y impact possible (step motor)
What is the precision that can be achieved
 simulation

## Slide 13: Tuning the beam with an q angle offset
Standard tuning:
Beam on optical axis
Kicked beam:
TH2KX1 and HADKX1
TH2KX1:
2 mrad kick
Incident angle at the pion production target = - 8 mrad
TH2KX1:
1 mrad kick
HADES p beam line
Incident beam line
HADES X-Y detectors
HADES LH2 target
X-Y diagnostic box
Scint.

## Slide 14: Determining the non-dispersive 1st order coefficients
Specific Simulation software
Inputs:
  Max Angle of incidence: Dq = 8 mrad (or Dj = 7 )
  Max Width of angular divergence: dq = 1 mrad (or dj = 4 mrad)
  Max Impact abscissa of beam at p production target: Dx = 0.2 cm (or Dy = 0.1 cm)
  Max Width of beam at p production target: dx = 0.05 cm (or dy = 0.05 cm)
  Number of recorded events (N=106)
  Number of points (5 assumed)
Minimizing where :
  Dxi and Dqi are central values of beam distributions at the p production target
  Xdet are measured positions (include dq and dx beam distributions around the central values )
  No sizeable geometrical abberations (T122, T124, T344 , etc. very small)  no need to add more q values
Outputs
  Tij distributions
  12 parameters (6 in horizontal plane and 6 in vertical plane)
X
q

## Slide 15: Precision on coefficients
Test case (keeping Dx = 0.)
dT12 / T12 ≈ dx / ( N1/2 T12 Dqmax )/T12 where N is the counting rate
 << 1%
Precision of determination can turned down as low as reasonably possible
Systematic biases: taken into account later through a simulation
Beam H size
Beam angular offset

## Slide 16: Results for detector 1 (d=0)
Tij | Theor. value | Fitted m value | Fitted s value | Relative precision on m
T11 | -1.782 | -1.777 | 2.533 | 0.15 %
T12 | -4.835 10-2 | -4.835 10-2 | 6.32 10-3 | 0.01 %
T33 | -18.6 | -18.58 | 46.4 | 0.25 %
T34 | -3.84 10-3 | -3.77 10-3 | 6.6 10-2 | 1.7 %
N= 106 events
dm = s / (N)1/2
T11
T12
T33
T34

## Slide 17: Results for detector 2 (d=0)
Tij | Theor. value | Fitted m value | Fitted s value | Relative precision on m
T11 | -0.924 | -0.909 | 12.0 | 1.3 %
T12 | -0.477 | -0.477 | 0.03 | < 0.01 %
T33 | -69.9 | -70.0 | 245 | 0.35 %
T34 | -0.8523 | -0.8519 | 0.35 | 0.04 %
N= 106 events

## Slide 18: Comments on the requested beam initial conditions
Dx, Dq
  No real measuring device at the p production target  2 options
  Only MIRKO-based estimates from kicker currents in TH2KX1 and HADKX1 and measured position on 2 ‘detectors’ (grid and scintillator)
  Beam always centered on the scintillator (access to T12 only )
Dy, Dj
  Scintillator step motor gives access to y position; precision?
  Comparison with MIRKO calculations will help controlling the H plane
KIckers
Detectors

## Slide 19: Extracting 2nd order coefficients: T116, T126, T146, T336, T346
Tune the HADES beam line to d=-2% and minimize the quantity
where
 determination of T’11 and T’12 and extraction of T116 and T126 by
effect of 2nd order contribution; =0.5- 1.5 cm
 extraction of 10 parameters (5 coeff × 2 detectors)
T16 and T166 are known with high precision

## Slide 20: Systematic error propagation (I)
Question: Can uncontrolled systematic offsets lead to a wrong determination of coeeficients and then to an uncorrect momentum determination
  When extracting coefficients, we may have systematic biases when tuning the beam for different incident angle and position
  we do not have full localization capabilities in a magnet-free region
    d: most likely very low (<< 1%) (localization of beam irrelevant)
    q: 1 mrad over 8 mrad (< 20%)
    j: 1 mrad over 8 mrad (< 20%)
    x: < 0.2 mm (<50% of image size)
    y: < 0.2 mm (<50% of image size)
  Systematic study for all coefficients (8 in H plane and 7 in V plane) at the 2 detector locations
    1st order dispersion term T16 and T36 changed by 10%
    1st order magnification terms (T11 and T33) changed by 50%
    All other terms changed by 20%

## Slide 21: Systematic error propagation (II)
No noticeable effect seen
  absolute shift on pion momentum smaller than 0.01%
  Resolution unchanged
2 exceptions
  T16: changing its value by 10% shifts the extracted d value by 0.1% at d=2% (effect comparable to the resolution)
  T33: changing its value by 50% influences the resolution, but only at a given d value (compensation effect between the T33 and T346 terms)
µ=3.8% (4%)
µ=1.91% (2%)
µ=-3.8% (-4%)
m=1.94 % (2%)
s=0.23% (0.1%)
Momentum offset d (%)
Momentum offset d (%)

## Slide 22: Beam time estimate
Proton beam
  3.5 GeV
  Low intensity (< 104 pps to fit within the DAQ capabilities)
Dispersive terms: T16, T36, T166, T366, X0, Y0
5 values of d  4 hours  12 parameters (6 per detector)
Horizontal coupling terms: T11, T12, T32, T116, T126
10 measurements = 5 in (x,q) × 2 in d  6 hours
10 parameters
vertical coupling terms: T14, T33, T34, T146, T336, T346
 10 measurements = 5 in (y,j) × 2 in d  6 hours
12 parameters
TOTAL of 2 shifts for measuring 34 parameters

## Slide 23: Conclusion and outlook
Control of the calculated transport coefficients possible
Errors on d induced by systematic errors very small or easily handable
Importance of measuring the offset parameters (absolute calibration of pcent)
To do
  Better treatment of multiple scattering effects ; detector 1 off the focus  result in 2 weeks
  Prepare the programs for fitting during the may beamtime

## Slide 24: Spare slides
Individual contributions in the X plane
Individual contributions in the Y plane
X-Y occupancy plots
Table of coefficients
The system of 4 equations

## Slide 25
T11
T12
T13
T14
T16
T111
T112
T122
T123
T124
T126
T133
T114
T116
T113
T134
T136
T144
T146
T166
Only 8 terms contribute significantly : i.e. > 0.5 × detector resolution)
Contibution (mm)
Contibution (mm)
Detector 1
resolution
( = 0.8 mm)
Individual contributions in X
Detector 2 resolution
( = 0.8 mm)
Index
numbering scheme
X
q
Y
j
-
d

## Slide 26
T31
T32
T33
T34
T36
T311
T312
T322
T323
T324
T326
T333
T314
T316
T313
T334
T336
T344
T346
T366
Individual contributions in Y
Only 7 terms contribute significantly : i.e. > 0.5 × detector resolution)
Contibution (mm)
Contibution (mm)
Detector 2 resolution
( = 0.8 mm)
Detector 1 resolution
( = 0.8 mm)

## Slide 27: Space occupancy at detectors
condition at Q9
|x| , |y| < 6 cm
Condition at HADES:
|x| , |y| < 6 mm
Good events are well inside :
Silicon Detector 1 and Detector 2
LH2 entrance window
Some good events cut (< 10%) by size of diamond detector (15*15 mm2)
Light yellow zones correspond to the detector size
Entrance window of LH2 is 1 m ahead of LH2 target
Diamond detector is 0.4 m ahead of LH2 target
Try to move as close as possible to LH2 target

## Slide 28: Values of the important coefficients
10-1
Several values have been corrected
(orders of magnitude !?
10-2
10-2
10-1
10-1
10-2
10-2
10-1
10-2
10-2
10-2
10-2
10-1
10-2
10-2
10-1

## Slide 29: The 4 equations