DAQ: Status of Upgrade
Outline
EU-Contract and BMBF money
Readout and IPU-boards
  - MU V2
  - TOF-Readout and IPU
TRB V2
  - Test-Board for TRB_V2
Trigger Distribution
  - Trigger-Adapter (old to new bus)

---
Upgrades (DAQ-point of view) / EU
EU-FP6 Construction Contract
Resistive Plate Chamber / RPC ->Coimbra/Santiago
  - TRB V2
Forward Wall -> Frankfurt
DAQ-Upgrade -> GSI
  - TOF Readout / Trigger
  - MU V2
  - VME CPUs (45k€)
BMBF (Bundesministerium für Bildung und Forschung)
MDC Readout / Trigger
RICH Readout / Trigger

---
List of Projects
Aim: 20 kHz primary data rate to ensure measuring rare decays in heavy systems

---
EU-Contract: Where we are now?
Money spent (invest) by me on the account of others in 9 month (2005-10-01 til 2006-07-01):
Duration of DAQ-work: 25 month

---
Milestones

---
Important Milestones and Time left
M4: TOF IPU and readout functionality operational
  - due in month 14 of project
  - 5 month to go for Ingo
M5: MU V2 in operation
  - due in month 15 of project
  - 6 month to go for Marek
M6: Eventbuilder operational (distributed)
  - due in month 17 of project
  - 8 month to go for Sergej
M1 of RPC project: Readout-Board freeze-out
  - already due, not finished: expected in 1 month.
Conclusion: Could be possible without TRB_V2!

---
ETRAX_FS_DEV1
Purpose:
  - Validate Etrax-FS I/O-Co-Processor
  - Translate between old-Trigger-bus and new optical trigger-bus
  - Connectivity to Concurrent-VME-CPU (Acromag)
Status:
10 assembled boards available (5 Ethernet connectors are missing)
Power, clock, reset-logic => OK
Cross-compiler and kernel are available
currently worked on in Krakow and GSI

---
Status I, Etrax-FS-DEV1 and Trigger-converter

---
Timeschedule

---
Other things....

---
Architecture
DC/DC
48V
TRB V1.0
TDC
32
channels
Computer +
Memory +
Flash +
Network
FPGA
FIFO
Dual Ported RAM
TDC
32
channels
TDC
32
channels
TDC
32
channels
Ethernet
Triggerbus

---
TRB Module and components
4*32 channels TDC, HPTDC
80 pin twisted pair cable, KEL connector
Single Chip Computer with Ethernet
FPGA
DC/DC 48V, isolated
Memory

---
Results II
Performance:
  - sigma between 2 channels (4 TDCs): 38ps
  - LVL1 readout of 60 TDC-words/event: 35kHz
  - LVL2 readout of 60 words/event: 5-6kHz
  - LVL2 readout of empty events: 18-19kHz
  - all without DMA, no optimization in FPGA
TDC-Resolution
  - sigma between 2 channels (4 TDCs): 38ps
  - no signs of crosstalk on TRB (has to be verified with more careful measurement)
  - RPC-detector channel resolution: 80ps

---
Future: TRB V2
TRB V2.0
TDC
32
channels
Computer +
Memory +
Flash +
Network
large FPGA
Virtex 4
LX100
TDC
32
channels
TDC
32
channels
TDC
32
channels
Ethernet
Trigger and
IPU data
over optical
 link
DSP /
Tiger Sharc

---
Future II
Additional Features:
  - 2 Gbit optical link for online pattern-recognition data transfer and LVL1 and LVL2 trigger information (not timing)
  - 3 times faster CPU (21€/piece)
  - Large FPGA for online pattern-recognition, zero suppression....
  - DSP: Tiger-Sharc (TOF-algorithm)
  - option: remove TDCs, connectors for readout of:
    - MDC, RICH
  - Clock-Distribution and Power-Sequence Chips: Lattice

---
Appendix
New Trigger Distribution and IPU-Data transport
  - http://hades-wiki.gsi.de/cgi-bin/view/DaqSlowControl/DaqUpgradeOverview
  - http://hades-wiki.gsi.de/cgi-bin/view/DaqSlowControl/NewTriggerBusNetwork

---
Summary
Things to learn from HADES-experiences:
  - Don't allow a zoo of digital-hardware for every subsystem
  - Data transport issues are at least 10 times more demanding/time-consuming than the algorithm to implement (maybe connected to the zoo of hardware)
  - Think more about Low-Voltage Power-Distribution

---
Description of Work, part 2
Faster TOF-Readout and TOF-IPU and faster Matching-Unit (Synergy)
  - VME-board with recent digital components (FPGAs, DSPs) to ensure needed performance
Necessary tasks:
  - Evaluation of algorithm for faster CPU [done]
  - One prototype PCB / tests
  - Production
  - Integration into HADES-DAQ
Manpower:
  - TOF:	Ingo Fröhlich, Univ. Frankfurt
  - MU:	Marek Palka, JU Krakow