## Slide 1: Implementing the multiple scattering in the pion beam line
T. Hennino, E. Atomssa
IPN Orsay
+ J. Biernat, J. Kempter
18/03/2014

## Slide 2: Simulation conditions
Inputs to the simulations
  All transport coefficients (1st and 2nd order)
  Full treatment of H and V planes (with all crossed terms)
  Detector location and thickness
Changes wrt previous calculations
  Detector 1 not at focal plane (effect of Multiple Scattering cancels out if at a focal plane)
  Focal inclination properly taking into account (T126 and T346 terms)
  Multiple scattering at the second detector (after Q7) included to
  calculate the position resolution at the HADES target

## Slide 3: Backpropagation to production target
Coordinates at detector 1 can be calculated from the formula
Dropping negligible contributions ( q2, qj, j2 ), the backpropagation can be done by writing (d is known in a simulation)
with
Solving the system gives the initial values x0, q0, y0, j0 , that include the effect of Multiple Scattering and that can further be used to calculate the position on detector 2
The same is done with detector 2 (including MS)and propagated back to production target then forward up to HADES target
Consistency checks made (initial q and j openings with no Multiple Scattering OK)
Multiple Scattering term

## Slide 4: Principle of the method
First part of beam line
Q1 to Q4 +
Dipole 1
Second part of beam line
Q5 to Q7 +
Dipole 2
p target
Step 1
qMS,1
Step 2
qMS,2
Step 3
Step 4
Step 5
HADES target
Third part of beam line
Q8 Q9

## Slide 5: Position resolution at HADES target: Preliminary results
Important increase of the spatial resolution
7 peaks corresponding to d = -6%, -4%, -2%, 0%, 2%, 4% and 6%
HORIZONTAL position resolution
VERTICAL position resolution
d | -4 % | -2 % | 0 % | 2 % | 4 %
H resolution | 5.4 mm | 5.2 mm | 5.2 mm | 5.2 mm | 5.0 mm
V resolution | - | 7.1 mm | 1.2 mm | 7.5 mm | -
-4 %
-2 %
0 %
2 %
4 %
6 %

## Slide 6: Conclusion and outlook
New Hbeam.h module including multiple scattering in any detector (E.A. T.H.)
  Tested in Orsay
  To be tested at GSI
Include the Diamond start detector information (3 X-coordinates + 3 Y- coordinates to access to the 5 unknown (x0,q0,y0,j0,d)  fit procedure
Get the new position at the HADES target with a better resolution (d, xH, qH, yH, jH )