Meeting of 08/10
Initial objectives
What has been done so far
Partial Conclusion
Investigation

---
Initial Objectives
- PID + effienciency correction for invariant mass spectrum
- Comparison with models : SMASH with acceptance filtering
- Interpretation

---
PHD Objectives
- Multidifferential Analysis : Multiplicity, pt , rapidity
- Angular Distribution → Polarization
- More ??

---
PID
- Comparison between data and simulation
- White leptons embedded
- No_enhancement : SMASH ( π0 , η)
- PLUTO embedded ( π0 , η)
-------> Focus on RICH related observables

---
Radius cut
Gaussian fit : 2 σ cut
For both simulation and data
19 < R < 27 mm
Normalized radius distribution before (red) and after selection (black)
Nothing Particular to say on this cut

---
NCALS cut
Double gaussian fit : G1 and G2 for experimental data
G1 : Isolated Pairs G2 : Close Pairs
Single gaussian distribution for white leptons -----> isolated pairs only
Only G1 to be used as G2 is related to background pairs
White leptons

---
NCALS cut
Efficiency of the cut on isolated pairs represented by G1
SMASH and data agrees
Need to have nearly same efficiency for a specific cut : ~ 99 %
8 < N < 24 : Used cuts
{ int to{Ncut} G1(N)dN } over { int to{Nmax} G1(N)dN }
Efficiency =
NCALS < 8 : Background noise to remove

---
NCALS cut improvement
Purity of isolated pairs is correlated to the maximum cals cut
Variate value by fixing the efficiency of the cut for simulation and data to be the same
Observe Improvements or not
Weird behavior with theta and phi correlation need to be investigated
Maybe try looking directly at RICH geometry ?
{ int to{Ncut} G1(N)dN } over { int to{Ncut} G1(N)+G2(N) dN }
Purity =

---
Possible Improvements
Understand Angle dependence for theta and phi
Possible angle dependent cut if successful
Difference in simulation and data --→ to check
NOT URGENT : AFTER RESULTS

---
ECal
- Need to estimate hadronic background
- RICH rotating method not available
- 2.5 out of 6 sectors available of ECal
 Impact on other observables
 Re/Define new cuts

---
Effective mass cut
Ratio Ecal / RPC only : using covered Ecal sectors
After selection
Very strict selection to obtain best purity:
Black lines : Pion theoretical mass
Cut Below pion lines to remove hadronic impurity
-----> Use of other beta cuts for systematics :
β > 0.95
β > 0.90
MetaMatchQualityEmc < 3
emc_index >= 0
Sector == 2/4/5
Eemc - pMDC > - 30 after 300 MeV

---
RICH Matching Track (RMQ)
Δθ = θMDC - θRICH
Cut Dependence :
Electron / positron
θ value : lower/higher half
Momentum
Modified Gaussian fit :
Enlarged distribution for SMASH compared to white, closer to experimental data
Constant background also presents → Close Pair effect ?

---
RMQ Parameter
 Mean of ɸ electron distribution has opposite trend depending on simulation and data --> possible wrong scattering correction (Joerg)
Mean : ɸ positron angle1
Mean : ɸ electron angle1
 Systematic deviation for σ :
Inherent difference, no important changes possible
Difference between white and SMASH
σ : ɸ electron angle1
σ : ɸ positron angle1

---
RMQ Parameter
Cut for Δθ and Δɸ distribution using 2σ of function fit : rectangular cut
 - Way of improving ---> Circular or elliptic cut using a maximum value :
sqrt((Δθ-Δθmean/Δθrms)2 + (Δɸ-Δɸmean/Δɸrms2) < 1
 - Using numerical integrations fix 95% cut instead of 2σ to better control efficiency issues
For now, cut efficiency vary between 10 and 30 % which is a problem
Difference between SMASH and white leptons :
Already investigated : Dalitz decay removed, change σ value closer to white one
Correlation between Dalitz decay and phase space distribution
Change directly phase distribution to SMASH one : observe or not changes in this parameter

---
Acceptance Efficiency Matrix
Method : White leptons
3D (θ,ɸ,momentum) matrix : 4π, In Acc, Reconstructed
InAcceptancebit(4,4,4,4,0,0) with smeared momentum
After PID selection for reconstructed
Acc = InAcc/4π
Eff = Rec/In Acc
1D momentum projection of acc/eff matrix

---
Self Consistency Check
Efficiency matrix consistency check with η PLUTO embedded :
Using InAcceptance method from Kine
Ratio of In Acceptance over after reconstruction spectrum boosted by efficiency factor from white lepton
Ratio close to 1 to 10 % except between 0.05 and 0 Region
Ratio of Invariant mass spectrum of η PLUTO embedded using efficiency correction and in acceptance filtering
Objective : - Cocktail scaled by multiplicities to cover full invariant mass spectrum and use it as a correction factor
   - Momentum Smearing for kine values

---
Background
K factor for charge dependence in sign-like background reconstruction
Signal over Background

---
SMASH
. Last minute problem resolved : Normalization
. Total number of π0 in full phase space and not only with opening angle > 9°
. Improve Statistics
. Use thermalization and Coarse Graining procedure and compare with this baseline
Normalized SMASH dilepton invariant mass spectrum

---
Comparison
Invariant mass spectra efficiency corrected
Invariant mass spectra uncorrected
My yield is systematicaly below Niklas -----> Investigate PID and efficiency in π0 region

---
Comparison
- π0 region : [0 , 0.2 GeV/c2] is underestimated compared to Niklas
- Differences in ɸ region : [0.9 , 1.1 GeV/c2] → Need to Investigate
- Efficiency correction is insufficient to for π0 region → Need to Investigate
- Coherent because SMASH filtered and my
Spectrum do not match in this region leading
To comparison problems
- ρ excess radiation is observable after π0 region
- ω melting seems important : need coarse graining
SMASH acceptance filtered and Niklas efficiency corrected spectra

---
TO DO
- Finalize RMQ analysis and simulations coherence understanding
- Resolve efficiency problem and π0 region underestimation
- Run new settings for SMASH
- Check BG simulation
- Start multidifferential analysis
- Start Angular distribution analysis