## Slide 1: Analysis of april 2014 run: experimental determination of beam line transport coefficients
E. Atomssa, T. Hennino, L. Hijazi, B. Ramstein
+ Lukas, Joana, Rafal, …
28/05/2014

## Slide 2: Aim and run conditions
Check the 1st and 2nd order transport coefficients at the 2 tracking detectors that allow to reconstruct the pion momentum (px, py, pz) at the HADES target
X= S Tij xj + S Tijk xj xk (or eq. Y= …)
  8 coeff. in H (T11, T12, T14, T16, T116, T126, T146, T166 )
  7 coeff. in V (T32, T33, T44, T36, T336, T346, T366 )
  X1, Y1, X2 and Y2  px, py, pz of each pion (see TDR)
7 different settings for the spectrometer part (-4.5 to +4.5 %)  determination of the dispersive terms T16, T166, T36, etc..
15 different settings for the incident beam line (before the pion production target)  determination of T11, T12, etc…
14 different settings (combination of incident beam line and spectrometer settings) for Tij6
In total 33 different combinations were measured
  Saturday campaign (only 5 out of 33)
  Wednesday campaing

## Slide 3: Analysis status
Production of root files (Joana, Lukas)
Consistency checks (2 independant analysis)
Analysis of the peaks (> 150 fits of strip distributions)
Analysis macros for determination of the coefficients written (most of them already tested and running)
First results on dispersion coeff. T16, T166, T36, T366 , already shown by Beatrice last meeting

## Slide 4: Open problems
Inconsistency between Saturday and Wednesday disp. Coeff.
  T16 (det1) -0.84  -0.79
Inconsistency between measurements made at more than an hour interval
  Position and widths affected coherently on all profiles  hope for correcting (or removing)
  Difficulties to determine second order coefficients
    Values can depend very much on the considered set
    Extreme sensitivity to ‘exact’ beam conditions (size of corresponding contributions lower than position shifts resulting from uncontrolled beam conditions at the level of a fraction of a mm or a mrad)

## Slide 5: remedies
More checks (several measurements were done 2 times)
Include additional offset parameters (complicated procedure  coupled analysis of X/Y det1/det2 position and width spectra)

## Slide 6: Conclusion and outlook
Need of a few more days
In parallel, simulation to be performed to analyze the impact of poorly known coefficients on the determination of px, py, pz and other physical variables ( s, MM)